## Slide 1
DLL
Nguyen Van Minh Tam, Tran Huu Anh Dong, Le Trung Luom
March 29th , 2021

## Slide 2: I. Contents
Comparison of C and DLL Block
Walkthrough to use method of DLL
Example
- Buck Converter
- Inverter

## Slide 3
How to do C programming in PSIM
3

## Slide 4
Comparison of C block and DLL block
We can do C programming by using C Block and DLL Block
In the system including many PI controller and algorithm, DLL Block is more effective than C Block
 | C Block | DLL Block
Advantages | Easy to use C programming | Short simulation time (about 60% of C Block’s simulation time)
Weakness | Long simulation time | Complex to use C programming (need other program like Visual studio)
4

## Slide 5
Walkthrough to use method of DLL with
Visual Studio 2019
Walkthrough to use method of DLL
5

## Slide 6
Walkthrough to use method of DLL
Step 1. Create a new DLL project file
Step 2. Make source code
Step 3. After compile and build, check if the DLL file is generated
Step 4. Save PSIM file in the path where contain the DLL file
Step 5. Enter to the File Name with DLL file name that we have created earlier.
6

## Slide 7
Using method of DLL (Prerequistes)
A computer that runs Microsoft Windows 7 or later versions.
Make sure that the Desktop development with C++ workload is checked. Don’t worry if you didn't install this workload when you installed Visual Studio. You can run the Visual Studio Installer again, click to Modify Button and install it now.
An understanding of enough of the fundamentals of the C/C++ language to follow along.
7

## Slide 8
Step 1. Create a new DLL project file
- Set Language to C++, set Platform to Windows, and set Project type to Library.
- Select Dynamic-link Library (DLL), and then choose Next.
Using method of DLL(1/5)
8

## Slide 9
Using method of DLL(1/5)
Step 1. Create a new DLL project file
9

## Slide 10
Step 2. Make source code
Using method of DLL(2/5)
10

## Slide 11
Step 3. After compile and build, check if the DLL file is generated
Using method of DLL(3/5)
Build: ctrl + B
11

## Slide 12
Step 4. Save PSIM file in the path where contain the DLL file
Using method of DLL(4/5)
12

## Slide 13
Step 5. Enter to the File Name with DLL file name that we have created earlier.
Using method of DLL(5/5)
13

## Slide 14
PI controller in continuous
time domain
Approximate the integral term
The discretized PI controller
Discrete PI controller
Discrete PI controller as C code
pi_error = Vo_ref – Vo;
pi_error_sum += pi_error;
pi_out = Kp*pi_error + Ki*Ts*pi_error_sum;
Transformer PI controller to C code
14

## Slide 15
EXAMPLE – BUCK CONVERTER
EXAMPLE
15

## Slide 16
System block diagram
Parameter of Buck converter: Vi = 820V, Vo = 180 to 800V, PO = 40kW, L = 400uH, C = 20 uF.
Goal is to control output voltage Vo in any condition with disturbance.
pi_error = Vo_ref – Vo;
pi_error_sum += pi_error;
pi_out = Kp*pi_error + Ki*pi_error_sum*Ts;
if(pi_out > 1) Duty = 1;
else if(pi_out < 0) Duty = 0;
else Duty = pi_out;
PI controller
Limiter Block
C code
C programs of PI and Limiter block:
16

## Slide 17
PWM_frequency=50000; // Swithcing frequency
if(PWM_Update > 0){
PWM_Ts=1/PWM_frequency;
PWM_TsCnt = (long)(PWM_Ts/delt);
PWM_CompA = (long)(PWM_TsCnt*Duty);
if(PWM_CompA < 0) PWM_CompA = 0;
PWM_Update = 0;
}
if(PWM_Cnt >= PWM_TsCnt){
PWM_Cnt = 0;
PWM_Update = 1;
}
else PWM_Cnt++;
if(PWM_Cnt > 0 && PWM_Cnt <= PWM_CompA ) {gate = 1;}
else gate = 0;
C programs of Carrier and Comparator Block
Carrier
Comparator
- PWM_TsCnt: is variable count
- PWM_CompA: is comparison waves
System block diagram
17

## Slide 18
in[0]
in[1]
in[2]
out[1]
out[0]
*in
*out
out[2]
C code for DLL
18

## Slide 19
Scheme of Buck converter for PSIM simulation
Parameter of Buck converter: Vi = 820V, Vo = 180 to 800V, PO = 40kW, L = 400uH, C = 20 uF.
19

## Slide 20
Start up
Line regulation
Load regulation
Reference regulation
Simulation results
20

## Slide 21
Percent Overshoot = 50%
Settling Time = 2 ms
Steady state of Vo = 320V
Simulation results – Start up
21

## Slide 22
Vi is decreased from 820V to 720V
Vo is decreased
pi_error is increased
( because pi_error = Vo_ref-Vo )
Duty is increased
Vo is decreased to 320V
Vi is increased from 820V to 720V
It is similar with before circumstance
Simulation results – Line regulation
22

## Slide 23
Load current (iLf) is increased
Vo is decreased
pi_error is increased
( because pi_error = Vo_ref-Vo )
Duty is increased
Duty is returned original value
Simulation results – Load regulation
23

## Slide 24
Vo_ref is increased from 320V to 500V
pi_error is increased
( because pi_error = Vo_ref-Vo )
3. Duty is increased
5. Vo is increased from 320V to 500V
Simulation results – Reference regulation
24

## Slide 25
EXAMPLE
INVERTER
25
Parameters​ | Values​
Input voltage [VL-L,rms]​ | 360~400​
Battery voltage [Vdc]​ | 820±10​
Load [kW]​ | 40​
Ig,max​ | 61Arms@220V​
Full-load efficiency [%]​ | 97.5% @,380VL_L,rms​
Peak efficiency [%]​ | 98.5%​
THD​ | ≤ 5%​
PFC​ | ≥ 99%​

## Slide 26
System block diagram
26

## Slide 27
//--- include library-----
#include <stdio.h>
#include <math.h>
#include <Clarke.h>
#include <PiCtrl.h>
CLARKE c;
//--- variable definition---
double Kp_I = -0.0118, Ki_I = 4.3009e-04;
double Kp_V = 0.064, Ki_V = 100; // PI Controller outerloop
static double pi_errord = 0., pi_errorq=0., pi_error_sumd = 0.,
pi_error_sumq = 0., pi_error_sumV = 0., pi_errorV = 0.;
double interruptCntMax, interruptCnt = 0, interrupt, fsamling, Ts;
double V_ref = 820.0, Vdc;
//---------------------------
double Van, Vbn, Vcn, Val, Vbe, theta;
double ia, ib, ic, id, iq, io;
double id_ctrl, iq_ctrl;
double ma, mb, mc;
int init = 1; // init functions
#define PI 3.14159
__declspec(dllexport) void simuser(t, delt, in, out)
double t, delt;
double* in, * out;
{
// insert your code here
//-------------------input pin definition----------------------
Van = in[0];
Vbn = in[1];
Vcn = in[2];
ia = in[3];
ib = in[4];
ic = in[5];
Vdc = in[6];
//-------------------abc to alpha beta for Grid Voltage------------
if (init == 1) {
CLARKE_init(&c);
//insert your init funtions
init = 0; }
//-------------------abc to alpha beta for Grid Voltage------------
CLARKE_FUNC(Van, Vbn, Vcn, &c);
theta = c.theta; // Range : -PI --> PI
//-------- abc to DQ axis for current at Converter side------------
id = 0.66667 * (ia * cos(theta) + ib * cos(theta - 2 * PI / 3) + ic * cos(theta + 2 * PI / 3));
iq = 0.66667 * (ia * sin(theta) + ib * sin(theta - 2 * PI / 3) + ic * sin(theta + 2 * PI / 3));
io = 0.66667 * (ia * 0.5 + ib * 0.5 + ic * 0.5);
C code for DLL (1/4)
C code for DLL (2/4)
27
C code for DLL

## Slide 28
C code for DLL (3/4)
C code for DLL (4/4)
//---------------------SAMPLING AND INTERRUPT-------------------
fsamling = 50e+3;//Nyquist sampling fsampling >= 2*Fswitching
Ts = 1 / fsamling;
interruptCntMax = 1 / (fsamling + delt);
interruptCnt++;
if (interruptCnt > interruptCntMax) {
interrupt = 1;
interruptCnt = 0;
}
else interrupt = 0;
if (interrupt)
{
//----------------outer loop, Vdc control-----------------------
pi_errorV = V_ref - Vdc;
pi_error_sumV += pi_errorV;
id_ref = Kp_V * pi_errord + Ki_V * pi_error_sumV * Ts;
//--------------PI CONTROLLER Inner-loop-----------------------
// ----------d - control------
pi_errord = id_ref - id;
pi_error_sumd += pi_errord;
id_ctrl = Kp_I * pi_errord + Ki_I * pi_error_sumd * Ts;
if (id_ctrl > 1) id_ctrl = 1;
else if (id_ctrl <-1.0) id_ctrl = -1.0;
else id_ctrl = id_ctrl;
id_ctrl = id_ctrl;
//-----------q - control------
pi_errorq = 0.0 - iq; // iq_ref = 0 for PFC
pi_error_sumq += pi_errorq;
iq_ctrl = Kp_I * pi_errorq + Ki_I * pi_error_sumq * Ts;
if (iq_ctrl > 1.0) iq_ctrl = 1.0;
else if (iq_ctrl < -1) iq_ctrl =-1;
else iq_ctrl = iq_ctrl;
//------------------- end of loop--------------------
//------------dq to abc for 3Phase - SPWM ---------------------
ma = id_ctrl * cos(theta) + iq_ctrl * sin(theta) + io;
mb = id_ctrl * cos(theta - 2 * PI / 3) + iq_ctrl * sin(theta - 2 * PI / 3) + io;
mc = id_ctrl * cos(theta + 2 * PI / 3) + iq_ctrl * sin(theta + 2 * PI / 3) + io;
}
//-------------------------Output definition--------------
out[0] = ma;
out[1] = mb;
out[2] = mc;
}
28
C code for DLL

## Slide 29
After passing the LCL filter
Before passing the LCL filter
29
Simulation results - Inverter

## Slide 30
Vlink (Vout)
Output Power (40kW)
30
Simulation results - Inverter

## Slide 31
31
Simulation results - Inverter

## Slide 32
Simulation results - Inverter